Low-Coherence Michelson's Interferometer
By Matt Ruby

Abstract:
A broadband interferometer may be used to balance or make the distance between the two interferometer arms equal. Using this method, you should be able to balance the arms of a Michelson's interferometer to within the coherence length of the source that is being used ( ~1-2 microns in our case). The calculated black-body coherence length is ~ 0.5microns. This article will describe the setup and properties of this interferometer.

Basics:
  The Michelson's interferometer uses the superposition principle of light to create interference fringes. The superposition principle states that when two beams of light over-lap, you can add the components of the input beams to get the output beam.
Coherence Length:
  The coherence length, Lc, is the distance over which the phase of the light becomes uncorrelated with itself. That is, consider the phase of a beam of light at two spatial points X1 and X2. If X2-X1 is less than Lc then the phases at the two points are (at least partially) correlated. If X2-X1 is greater than Lc then the phases at the two points are uncorrelated. Please take note that the average HENE laser has a Lc ~ 20cm, but spectrally broad light may have Lc of only a few microns. This means that for the broadband interferometer we will need to have the two beam paths in Fig(1) be equal to within the coherence length of the source, in order to observe interference patterns.
  Fig(1). Michelson's interferometer.

Fig(2) shows how the pin hole is used to modify the wave fronts so that they are more uniform in the transverse direction. This increases the transverse coherence area and allows the observation of the fringes over the entire transverse profile of the light beam while leaving the longitudinal coherence length essentially unchanged.

    Fig(2). On the left the wavefronts of the light have a small coherence area. On the right (after the pinhole) the wavefronts have a very much larger coherence area.

Set-Up: Source
  Before building the interferometer we must first build the light source that will be used by the interferometer. To start with, we will use a high-power broadband light source. This source will be mounted to an optical table so that there will be minimal vibrations acting on the set-up. (Please note: this go's for all the optics and mounts in this article.) After the high power source, you will want to focus as much light as you can through an ~100 micron pinhole. This will provide the necessary transverse modification to the light's wavefronts. It is best to use an achromatic, aspherical condenser lens with a short focal length to accomplish this. The light from the pinhole will be collimated, by placing another short focal length lens after the pinhole. The distance from the pinhole to the lens should be equal to the focal length of the lens. Note: for easy alignment, you may want to use translational stages to align the focusing lens, pinhole, and collimating lens.
          Fig(3). Source optical setup.
- Set-Up: Interferometer
  Building the interferometer is fairly simple, as shown in Fig(1). There is a beamsplitter, with two opposite sides blocked by mirrors. This interferometer will have one of these two mirrors on a translation stage, so that we can balance the distance of the two mirrors with the beamsplitter. Note: The system is easy to build, the first alignment is DIFFICULT

Alignment
  Take a ruler to roughly balance the interferometer mirrors. Slowly, move the translation mirror towards the point where you think the mirrors will be an equal distance from the center of the beamsplitter. Introduce the source light into the interferometer. Overlap the beam at two reasonably distant spatial points. Use a diverging lens on the output arm of the interferometer. You should see a roughly circular, roughly homogeneous white spot with (unless you're very lucky) no dark fringes. Slowly adjust the length of one of the two (mirror) arms until you see some dark fringe patterns.

Below is a picture of my beam correction optics AKA the system that collimates the white light source and modified the coherence area (in the transverse direction).

Fig(4). From left to right: iris, collimating lens, pinhole, condenser lens and light source.
Tips
                  -When balancing the mirrors arms GO SLOW! It may be time consuming, but if you go fast you’ll pass the fringes without seeing them.
  - -Use a power meter to maximize light through the pinhole.
    -Put an iris in front of the collimating lens so that you can adjust the beam diameter.
    -Use a diverging lens at the output of the interferometer so that it is easy to see the fringes.
    -Use a beamsplitting cube.

Sources
1. Fig(1);http://en.wikipedia.org/wiki/File:Spatial_coherence_pinhole.png
2. Bryan Boggs, uoregon Optics Teaching Lab
3. Fig(3); http://physics.schooltool.nl/irspectroscopy/images/michelson_interferometer.gif